Semi conductors

Semiconductors are the materials which have a conductivity between conductors (generally metals) and non-conductors or insulators (such as ceramics).

Semiconductors : Germanium(Solar cells) or silicon(electric Circuits)

## Types of Semiconductors
Semiconductors can be classified as:
- Intrinsic Semiconductor
- Extrinsic Semiconductor

Intrinsic Semiconductor : An intrinsic type of semiconductor material is made to be very pure chemically. It is made up of only a single type of element.

## Extrinsic Semiconductor
The conductivity of semiconductors can be greatly improved by introducing a small number of suitable replacement atoms called IMPURITIES. The process of adding impurity atoms to the pure semiconductor is called DOPING. Usually, only 1 atom in 107 is replaced by a dopant atom in the doped semiconductor. An extrinsic semiconductor can be further classified into:
N-type Semiconductor(Donars)
Mainly due to electrons
- Entirely neutral
- I = Ih and nh >> ne
- Majority – Electrons and Minority – Holes
- the electrons in the n-type semiconductor are the MAJORITY CARRIERS and holes are the MINORITY CARRIERS.
P-type Semiconductor
Mainly due to holes
- Entirely neutral
- I = Ih and nh >> ne
- Majority – Holes and Minority – Electrons

Hall Effect
Aim : See Record
Apparatus Required : See Record
Formula used : See record

Theory :

Principle of Hall Effect :
The principle of the Hall effect states that when a current-carrying conductor or a semiconductor is introduced to a perpendicular magnetic field, a voltage can be measured at the right angle to the current path. This effect of obtaining a measurable voltage is known as the Hall effect.

When a conductive plate is connected to a circuit with a battery, then a current starts flowing. The charge carriers will follow a linear path from one end of the plate to the other end. The motion of charge carriers results in the production of magnetic fields. When a magnet is placed near the plate, the magnetic field of the charge carriers is distorted. This upsets the straight flow of the charge carriers. The force which upsets the direction of flow of charge carriers is known as Lorentz force.
Due to the distortion in the magnetic field of the charge carriers, the negatively charged electrons will be deflected to one side of the plate and positively charged holes to the other side. A potential difference, known as the Hall voltage will be generated between both sides of the plate which can be measured using a metre.
The Hall voltage represented as VH is given by the formula:

### Hall Coefficient
The hall coefficient is positive if the number of positive charges is more than the negative charges. Similarly, it is negative when electrons are more than holes.
#### Applications of Hall Effect
Hall effect principle is employed in the following cases:
- Magnetic field sensing equipment
- For the measurement of direct current, Hall effect Tong Tester is used.
- It is used in phase angle measurement
- Proximity detectors
- Hall effect Sensors and Probes
- Linear or Angular displacement transducers
- For detecting wheel speed and accordingly assist the anti-lock braking system.

Procedure : See Record

Observation Table:

Calculations:

Precautions :

Result:

  Photo-electric Effect

Aim :
Apparaturs :
Formula Used :
Theory :
Procedure :
Observation :
Calculation :
Result :

Diffraction Grating

Aim : LASER : Light Amplification by Stimulated Emission of Radiation

Apparatus :

Formula Used :

Theory :

Procedure :
Observation :
Calculation :
Result :

Frank Hertz Experiment

Aim :